ß-Galactosidase Production

This example deals with ß-galactosidase (ß-Gal), an intracellular enzyme produced by Escherichia coli. This enzyme is normally produced by E. coli up to 1-2% of total cell protein under conditions of induction of the lac operon. Using genetic engineering, the level can go up to 20-25% of total protein. In this example, an easily attainable level of 10% is assumed.

ß-Gal has found limited industrial applications until now. It is mainly used in the utilization of cheese whey. More specifically, immobilized reactors with ß-Gal have been developed to convert lactose found in cheese whey to glucose and galactose, yielding a sweetened product which can be used as an additive to ice cream, egg-nog, yoghurt, and other dairy products. Another application of ß-Gal is in the treatment of milk products. A significant number of people are lactose intolerant and cannot digest milk or milk products. Production of lactose-free milk products (using ß-Gal reactors) allows those people to digest them.

This example analyzes a plant that produces 18,000 kg of ß-Gal per year in 134 batches.  Several files have been included with this example:

BGal01:  This file represents the process at an early stage of plant design. All equipment is in Design Mode, meaning that all equipment volumes and throughputs are calculated as opposed to being specified by the user.

BGal02:  This file shows the process after equipment sizes have been specified for key pieces of equipment. The BGal02 file was used to produce the tables and graphs in the rest of this document.

BGal03:  This file is the same as BGal02, except that final product formulation and packaging unit procedures have been added.

PROCESS DESCRIPTION (file BGal02)

Flowsheet Sections

A flowsheet section is a group of unit procedures that have something in common. For instance, the ß-galactosidase flowsheet has been divided into three sections: 
1) Fermentation, 
2) Primary Recovery, 
3) Purification (see below). 

All the unit procedure icons of the Fermentation section are displayed in black, while the icons of the Primary Recovery and Purification sections are displayed in blue and green, respectively. For information on how to specify flowsheet sections and edit their properties, please see Chapter 7.1 of the manual.

Fermentation Section

Fermentation media are prepared in a stainless steel tank (V-101) and sterilized in a continuous sterilizer (ST-101). A compressor (G-101) and an absolute air filter (AF-101) provide sterile air to the fermentor (FR-101). Gaseous ammonia is used as a nitrogen source.

Primary Recovery Section

The first step of the primary recovery section is cell harvesting to reduce the volume of the broth and remove extracellular impurities; it is carried out by a membrane microfilter (MF-101).  Since ß–galactosidase is an intracellular product, the next step is cell disruption, performed in a high-pressure homogenizer (HG-101).  After homogenization, a disk–stack centrifuge (DS-101) is used to remove most of the cell debris particles.  A dead-end polishing filter (DE-101) removes the remaining cell debris particles.  The resulting protein solution is concentrated by an ultrafilter (UF-101).

Purification Section

Next the product stream is purified by an ion exchange chromatography column (C-101). Then it is concentrated by a second ultrafiltration unit (UF-102) and polished by a gel filtration unit (C-102). A diafiltration unit (DF-101) exchanges the gel filtration buffer, and the protein solution is lyophilized in a freeze dryer (FDR-101).

OVERALL MATERIAL BALANCES

The table below provides information on raw material requirements for the entire flowsheet.  The quantities are displayed in kg/year, kg/batch, and kg/kg MP (main product). Around 86 kg of purified ß-Gal is produced per batch. Note the large amounts of buffers and WFI that are required per batch.

| BULK RAW MATERIALS (ENTIRE PROCESS) |
| --- |
| Raw Material | kg/yr | kg/batch | kg/kg MP |
| Process Water | 13,760,000 | 64,000.000 | 754.200 |
| Glucose | 1,320,745 | 6,143.000 | 72.391 |
| Salts | 220,590 | 1,026.000 | 12.091 |
| Ammonia | 84,925 | 395.000 | 4.655 |
| Water | 1,935,000 | 9,000.000 | 106.059 |
| WFI | 42,263,657 | 196,575.147 | 2,316.516 |
| Tris Buffer | 36,893,340 | 171,596.929 | 2,022.163 |
| NaCl (0.1 M) | 30,134,728 | 140,161.526 | 1,651.716 |
| NaOH (0.5 M) | 17,937,190 | 83,428.793 | 983.156 |
| NaCI (0.5 M) | 2,513,305 | 11,689.791 | 137.757 |
| TOTAL | 147,063,480 | 684,016.185 | 8,060.706 |
| MP = Main Product, which is purified ß-Gal in this case. |

The above table was extracted from the RTF version of the Materials & Stream Report.

PROCESS SCHEDULING

The figure below is an Equipment Occupancy chart generated by SuperPro Designer. It shows the execution of the various processing steps as a function of time for six consecutive batches. The overall batch time is approximately 184 h. The recipe cycle time (time between consecutive batches) is 36 h. The minimum recipe cycle time (minimum time interval between consecutive batches) is 34.24 h and is determined by P-18 (in V-107), which is the time bottleneck. The number of batches per year is 215. All this information is displayed on the Recipe Scheduling Information dialog that is displayed by selecting Tasks\Recipe Scheduling Information.

Please note step P-17 utilizes two tanks (V-104 and V-104b) that operate out of phase (in staggered mode) to reduce the recipe cycle time. Staggered equipment is specified through the "Stagger Mode" box of the Equipment Data dialog of a procedure (right click on a procedure icon and select Equipment Data). Tank V-104 is the only one displayed on the flow diagram. Tank V-104b is visible on the Equipment Occupancy chart (see below). Step P-18 utilizes two tanks operating is stagger mode as well.

In addition to the above Equipment Occupancy Chart, SuperPro generates and operations Gantt chart that provides a detailed visual display of the execution of the various operations in the context of their procedures (see figure below).

COST ANALYSIS AND ECONOMIC EVALUATION

The key results of cost analysis for a plant producing 18,244 kg of ß-Gal per year follow.  This analysis assumes that a new facility will be built for this process, and the project lifetime is 15 years.

| EXECUTIVE SUMMARY (2004 prices) |
| --- |
| Total Capital Investment | 85,193,000 | $ |
| Capital Investment Charged to This Project | 85,193,000 | $ |
| Operating Cost | 103,102,000 | $/yr |
| Production Rate | 18,244.49 | kg MP/yr |
| Unit Production Cost | 5,651.14 | $/kg MP |
| Total Revenues | 182,445,000 | $/yr |
| Gross Margin | 43.49 | % |
| Return On Investment | 64.24 | % |
| Payback Time | 1.56 | years |
| IRR (After Taxes) | 51.17 | % |
| NPV (at 7.0% Interest) | 319,962,000 | $ |

The above table was copied from the Economic Evaluation Report generated by SuperPro Designer.  This table gives an overall summary of the economics of the process.  The information above (as well as additional information) is also displayed on the Executive Summary dialog (View\Executive Summary).

Much more detailed information is available in additional tables of the Economic Evaluation Report and the Itemized Cost Report.  One such table is the Annual Operating Cost summary shown below.  This breaks down the costs into general categories.  From this table, it is clear that consumables are the most important cost. The cost of raw materials is in the second position and facility-dependent costs in the third. Facility-dependent costs account for depreciation, maintenance, local taxes, etc.

| ANNUAL OPERATING COST (2004 prices) |
| --- |
| Cost Item | $ | % |
| Raw Materials | 18,162,000 | 17.62 |
| Labor-Dependent | 10,303,000 | 9.99 |
| Facility-Dependent | 13,980,000 | 13.56 |
| Laboratory/QC/QA | 1,484,000 | 1.44 |
| Consumables | 58,320,000 | 56.57 |
| Waste Treatment/Disposal | 448,000 | 0.43 |
| Utilities | 406,000 | 0.39 |
| Transportation | 0 | 0.00 |
| Miscellaneous | 0 | 0.00 |
| Advertising/Selling | 0 | 0.00 |
| Running Royalties | 0 | 0.00 |
| Failed Product Disposal | 0 | 0.00 |
| TOTAL | 103,102,000 | 100.00 |

The table below (also extracted from the Economic Evaluation Report) provides detailed info on the cost of consumables. It is obvious that the chromatography resins are the major contributors of this cost.

| VARIOUS CONSUMABLES COST (2004 prices) |
| --- |
| Consumable | Units Cost ($) | Annual Amount |  | Annual Cost ($) | % |
| Dft DEF Cartridge | 600.000 | 215 | item | 129,000 | 0.22 |
| MF Membrane (Biotech) | 600.000 | 688 | m2 | 413,000 | 0.71 |
| UF Membrane (Biotech) | 800.000 | 559 | m2 | 447,000 | 0.77 |
| INX Biotech Resin | 1,500.000 | 17,568 | L | 26,352,000 | 45.19 |
| Gel Filtration Resin | 800.000 | 38,723 | L | 30,978,000 | 53.12 |
| TOTAL |  |  |  | 58,320,000 | 100.00 |

The Itemized Cost Report displays breakdowns of various costs for each section of the process.  For instance, the table below provides information on the contribution of the Fermentation, Primary Recovery, and Purification sections to the process costs. The Purification section contributes 83.5% of the total operating cost. Overall, around 91.7% of the total operating cost is associated with the Primary Recovery and Purification sections. This is quite common for high-value biological products produce using E.coli.

| SUMMARY PER SECTION |
| --- |
| Section | $/kg MP | $/batch | $/year | % |
| Fermentation Section | 468.571 | 39,762 | 8,548,831 | 8.29 |
| Primary Recovery Section | 464.265 | 39,397 | 8,470,287 | 8.22 |
| Purification Section | 4,718.301 | 400,386 | 86,083,013 | 83.49 |
| TOTAL | 5,651.137 | 479,545 | 103,102,131 | 100.00 |

THROUGHPUT ANALYSIS

The Throughput Analysis Report (THR) and the corresponding charts provide information on equipment capacity and time utilization and identify the likely throughput bottleneck. For instance the figure below displays the Utilization chart that is generated by selecting View\Throughput Analysis Charts\Utilization. The blue color corresponds to size/throughput utilization, the cyan to time utilization, and the magenta to combined utilization. Column C-101 is identified as the most likely throughput bottleneck because it has the highest combined utilization (the product of capacity and time utilization). Please see the User’s Guide and/or consult the Help Facility for more information on throughput analysis and debottlenecking.

PRODUCT FORMULATION, PACKAGING, AND DISTRIBUTION

The BGal-c design case file displays a modified version of the base case flowsheet that includes unit procedure models for product formulation, packaging, and distribution. Most of these models are rather simple and their primary objective is to capture the cost associated with such process steps.

Product formulation and packaging operations often involve formation and use of discrete entities, such as tablets, bottles, boxes, etc. The flow of such entities is represented by discrete streams, which by default are displayed in blue color. For more information on discrete streams and entities, please consult the Help Facility and the User’s Guide.

To become familiar with the formulation and packaging unit procedure models and the concepts of discrete streams and entities, please open the BGal-c design case and visit the simulation data dialog windows of these objects. You can do that by right clicking on the various packaging unit procedure icons and their corresponding streams and selecting Operation (or Simulation) Data. Notice the different interface of discrete streams, which display the flow of discrete entities as well as the equivalent bulk flow (based on the bulk ingredients that compose the discrete entities).